## Slide 1: Electroencephalography Frequency Analysis
Taylor Baum

## Slide 2: Electroencephalography

## Slide 3: Electroencephalography detects electrical activity in the brain.
Notes: https://www.istockphoto.com/photos/eeg-test

## Slide 4: Let’s try and understand what exactly an electroencephalogram is detecting!
Notes: https://www.researchgate.net/figure/EEG-and-EOG-responses-to-visual-stimuli-a-red-spot-and-a-black-and-white-contrasting_fig1_226078506

## Slide 5: In the brain, we have neurons that are oriented in all different directions, and they transfer information between one another through electrical signals.

## Slide 6: The electrical potentials contained in neurons are generated by differences in concentrations of charge across cell membranes known as ion gradients.
Notes: https://www.https://bio1152.nicerweb.com/Locked/media/ch48/gradients.html.com/watch?v=Jk_9IhHVOTk

## Slide 7: First, let’s think about voltage and current, both which result from the ion gradients.
V = IR
Voltage = Current * Resistance

## Slide 8: Voltage (V in Ohms) is the difference in electrical potential between any two points in an electrical circuit.
V = IR
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 9: Current (I in amps) is the speed or rate at which the electrons flow through a resistor.
V = IR
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 10: To reemphasize the definition of voltage and current, we consider a water analogy.
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 11: For water to move through a hose (current to flow), there needs to be a difference in pressure (voltage) between two locations in the pipe.
High Pressure
Low
Pressure
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 12: If there is no difference in pressure (voltage), then there is no flow (current) through the pipe.
Low
Pressure
Low
Pressure
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 13: The existence of the pipe is the resistance to flow.
Low
Pressure
Low
Pressure
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 14: So, we can account for all three components of ohm’s law here.
V = IR
Notes: https://battlebornbatteries.com/amps-volts-watts/

## Slide 15: This concept is equivalent for electrical signals in neurons.

## Slide 16: There needs to be some difference in charge concentration between two points in the neuron for electrical charge to flow (current).
High Pressure
Low
Pressure
Large Positive Charge
Small Positive Charge
or Negative Charge

## Slide 17: Think of this flow of charge as a transfer of information. With no flow, there is no information being transferred.
High Pressure
Low
Pressure
Large Positive Charge
Small Positive Charge
or Negative Charge

## Slide 18: Any questions about:   electrical signals   voltage   current   neuronal communication

## Slide 19: An action potential is when the membrane voltage of a neuron gets positive enough that a wave of positive ions moves through the neuron.

## Slide 20: In order for flow or an action potential to happen, a big enough membrane potential or difference in charge is needed.

## Slide 21: EEGs don’t detect the action potential, but instead detect charge build-up in the extracellular space resulting, in the excitatory case, from the hypopolarization of the intracellular space.

## Slide 22: More generally, EEGs detect the build up of charge leading either to a neuron firing (Excitatory Postsynaptic Potential EPSP) or a neuron becoming less likely to fire (Inhibitory Postsynaptic Potential IPSP).

## Slide 23: Let’s consider the Excitatory Postsynaptic Potential in a cell that is oriented on the cortex according to the figure below.

## Slide 24: For EPSPs, the post-synaptic potential of a neuron must cross a threshold of -55 mV before the neuron will fire.

## Slide 25: Before a neuron reaches that -55 mV threshold, there are positive ions rushing into the neuron increasing the membrane potential and creating a negative charge outside of the cell.

## Slide 26: In a portion of a neuron that is away from the negative extracellular region, those positive ions are flowing out of the cell, creating a positive charge externally.

## Slide 27: This difference in charge should remind us of what we mentioned earlier.
High Pressure
Low
Pressure
Large Positive Charge
Small Positive Charge
or Negative Charge

## Slide 28: While this difference in charge eventually leads to an action potential, it is the existence of the difference in charge that the EEG picks up.

## Slide 29: The single electrical dipole created in one neuron isn’t strong enough for an EEG to detect it.

## Slide 30: But, there are special neurons near the surface of the brain called pyramidal neurons that are all oriented in the same direction.
Notes: https://www.mayoclinic.org/tests-procedures/eeg/about/pac-20393875

## Slide 31: So instead of single neuron recordings, we look at the summed activity of many pyramidal neurons.

## Slide 32: So instead of single neuron recordings, we look at the summed activity of many pyramidal neurons.
Notes: https://www.mayoclinic.org/tests-procedures/eeg/about/pac-20393875

## Slide 33: So instead of single neuron recordings, we look at the summed activity of many pyramidal neurons.
Notes: https://www.mayoclinic.org/tests-procedures/eeg/about/pac-20393875

## Slide 34: It is also important to keep in mind that EEG signals result from synchronous activity within the pyramidal neurons.

## Slide 35: For your BCI project, you are interested in EEG signals specifically coming from the occipital lobe, where visual signals are processed.
Occipital Lobe
Notes: https://www.wikiwand.com/en/Occipital_lobe

## Slide 36: Now we have an idea about where the EEG signal comes from, physiologically.

## Slide 37: Now let’s consider the frequency domain features being used in the SSVEP literature we have been reviewing.

## Slide 38: Frequency Analysis

## Slide 39: Frequency analysis is a field with which we convert a signal from the time-domain into the frequency domain.
Notes: https://www.nti-audio.com/en/support/know-how/fast-fourier-transform-fft

## Slide 40: The most often understood method for doing this is known as the Fourier Transform.

## Slide 41: Here we have a continuous time signal being transformed into a continuous frequency representation.

## Slide 42: For implementation of the fourier transform, we must consider a different version of this function known as the Discrete Time Fourier Transform (DTFT).

## Slide 43: Here we have a discrete time signal being transformed into a continuous frequency representation.

## Slide 44: The DTFT can only be implemented in real life by considering samples of the output of the DTFT, which is known as the Discrete Fourier Transform (DFT).

## Slide 45: Now, we have a discrete time signal being transformed into a discrete frequency representation.

## Slide 46: In order to do frequency-analysis of a real signal, we have to window the signal, and then sample the spectrum with the Discrete Fourier Transform.

## Slide 47: The Fast Fourier Transform (FFT) is a method of implementation of the Discrete Fourier Transform.

## Slide 48: Any questions about: Fourier Transform DFT DTFT FFT

## Slide 49: Spectral Estimation

## Slide 50: In each of these transformations, we are assuming that we have a deterministic signal, meaning that there is no randomness in the realizations of the signal.

## Slide 51: In our problem, our signals are inherently random, and as such, we must take that into account when doing frequency analysis.

## Slide 52: We won’t go exactly into the details, but a method to estimate the power spectral density of random signals is with the periodogram.

## Slide 53: The periodogram is the natural way to estimate the power spectral density, but we can do better.

## Slide 54: This illustrates an autoregressive process of order 6 used to illustrate the characteristics of the spectral estimation techniques I will show..

## Slide 55: The periodogram is a biased estimate of the PSD because its expected value is the frequency convolution of the true PSD with the DTFT of the autocorrelation of the data window.
Notes: Section 10.5.2 of Discrete-time Signal Processing by Oppenheim

## Slide 56: It is, however, asymptotically unbiased.
Notes: Section 10.5.2 of Discrete-time Signal Processing by Oppenheim

## Slide 57: The variance of the periodogram is asymptotically proportional to the square of the true underlying PSD.

## Slide 58: Consequently, the periodogram is asymptotically unbiased but not a consistent estimate.

## Slide 59: Consequently, the periodogram hits the peaks pretty well, but is very spiky throughout the estimate.

## Slide 60: There is a technique known as multitaper spectral analysis which is able to tighten up (reduce the variance) the estimate of the power spectrum.

## Slide 61: Given L “good” and “uncorrelated” windows, the multitaper spectral estimate formed by averaging the corresponding L tapered estimates would have a variance reduced by a factor L.

## Slide 62: We see a reduction in variance in the resultant spectral estimate.

## Slide 63: We have introduced a concept, multitaper frequency analysis which is complex, but quite straightforward to implement.

## Slide 64: Interactive Tutorial

## Slide 65: Resources Used
Buzsáki, György; Anastassiou, Costas A.; Koch, Christof (2012). The origin of extracellular fields and currents — EEG, ECoG, LFP and spikes. Nature Reviews Neuroscience, 13(6), 407–420. doi:10.1038/nrn3241
https://www.mayoclinic.org/tests-procedures/eeg/about/pac-20393875
https://battlebornbatteries.com/amps-volts-watts/
Britton JW, Frey LC, Hopp JLet al., authors; St. Louis EK, Frey LC, editors. Electroencephalography (EEG): An Introductory Text and Atlas of Normal and Abnormal Findings in Adults, Children, and Infants [Internet]. Chicago: American Epilepsy Society; 2016. Available from: https://www.ncbi.nlm.nih.gov/books/NBK390354/